## Slide 1: An evaluation of power performance for a small wind turbine in turbulent wind regimes
Nicholas J. Ward
Ph.D. Student, Energy Engineering
Advisor: Dr. Susan W. Stewart
The Pennsylvania State University

## Slide 2: Why study turbulence?
Increased attention towards engineering and economic feasibility in lower wind speed regimes [Ewing et al (2008)]
Progressive damage and shortened turbine lifetime via stochastic loads [Saranyasootorn & Manuel (2008)]
Increased interest in turbulence for future academic study [Web of Science]
  180 publications in 2014 (top)
  1400 cited articles in 2014 (bottom)
Publications
Citations
Year

## Slide 3: Wind Turbine & Site

## Slide 4: Methodology
Collect site characteristics data from wind turbine location
Determine relationship between P and TI
Quantify statistical distribution of in situ TI frequency
Verify/compare results with IEC standards, Albers (1997) and Sunderland et al (2013)

## Slide 5: The turbine power and turbulence intensity were quantified over 15 months (6/13-9/14). Excluding anomalies like turbine maintenance, power exhibits strong statistical correlation with turbulence intensity.

## Slide 6: Seasonal Variation of Power & Turbulence Intensity

## Slide 7: Common industrial practice requires a Weibull distribution for frequency of wind speed [Woolmington et al (2014)]. However, an empirical distribution match for turbulence intensity is more difficult.

## Slide 8: Wind speed dependence for the turbine power curve enables statistical correlation between frequency of occurrence for power and TI.

## Slide 9: The culmination of these turbulence intensities at constant velocities enable “binning” of turbine power output. With smaller wind speeds, the power output increases for increased TI, exhibiting periods of overdrive.

## Slide 10: Turbulence intensity tends to follow a Gamma distribution (k=12, θ=0.014) at constant wind velocity.

## Slide 11: Relative Error Between Gamma Function and Observed TI
Wind Speed (m/s) | Min Error (%) | Max Error (%) | Mean Error (%)
5.00±0.25 | 0.00 | 1.66 | 0.45
7.50±0.25 | 0.00 | 1.67 | 0.42
10.0±0.25 | 0.00 | 3.18 | 0.79

## Slide 12: Example of TI Integration into Wind Turbine Power Curve

## Slide 13: Conclusions & Future Work
The gamma function is a good indicator to estimate power performance incorporating TI
Power output increased by as much as 60% for lower wind speeds at higher TI, but decreased power by as much as 17% for high wind speeds and TI
A more standardized approach for TI integration into the power curve was tested and correlated well with results from Sunderland et al (2013) and Albers (1997)
Over-performance is possible for low wind speed regimes with high TI
This process can be integrated into (or verified by) industry accepted programs like WT_Perf and FAST for computer simulations predicting stochastic loads due to turbulence and their effects on power production for any turbine size in any location

## Slide 14: Acknowledgments
Research advisor: Dr. Susan Stewart
Mr. Brian Wallace
Aerospace & Energy Engineering Departments
Penn State Center for Sustainability

## Slide 15: References
Ewing et al (2008). “Analysis of Time-varying Turbulence in Geographically-dispersed Wind Energy Markets.” doi:10.1080/15567240701232162
Saranyasootorn & Manuel (2008). “On the propogation of uncertainty in inflow turbulence to wind turbine loads.” doi:10.1016/j.jweia.2008.01.005
Web of Science
Manwell et al (2010). “Wind Energy Explained: Theory, Design and Application.” 2nd Edition. ISBN: 978-0-470-01500-1
Wang et al (2014). “A new turbulence model for offshore wind turbine systems.” DOI: 10.1002/we.1654
Woolmington et al (2014). “The progressive development of turbulence statistics and its impact on wind power predictability.” doi: 10.1016/j.energy.2014.03.015
Albers (1997). “Turbulence and Shear Normalisation of Wind Turbine Power Curve.”
Sunderland et al (2013). “Small wind turbines in turbulent (urban) environments: A consideration of normal and Weibull distributions for power prediction.” doi:10.1016/j.jweia.2013.08.001

## Slide 16: Questions?

## Slide 17: Quantifying Power and Turbulence
Turbine power (P) is a function of the cube of the velocity (v), air density (ρ) and rotor area (A) [Manwell et al (2010)]
Turbulence intensity (TI) is the ratio of the standard deviation (σ) to the mean wind speed (V) [Wang et al (2014)]
It can therefore be quantified that turbine power can related to turbulence intensity

## Slide 18: Sunderland et al (2013) Key Figure

## Slide 19: Albers (1997) Key Figure