## Slide 1
Design and Development of an Integrated Avian and Bat Collision Detection System for Wind Turbines
Robert Suryan, Roberto Albertani, Brian Polagye,
Jeremy Flowers, Trevor Harrison, Concong Hu, William Beattie
© M. Mirinha/STRIX

## Slide 2
On Land
Avian and Bat Mortality
Assessment via carcass surveys
Effective but problematic on land
Not effective at sea
At Sea

## Slide 3
Optical Node
Stereo Infrared & Visual Spectrum Cameras
Remote Transmission of “Event” Data
Central Processing Onboard Turbine
Onboard Synchronized Sensor Array
Bioacoustics Node Acoustic and
Ultrasonic Microphones
Vibration Node Accelerometers &
Contact Microphones
Notes: Cameras in stereo allow distance and size estimates of targets

## Slide 4
System Configuration
Accelerometers
Contact Microphones
Camera
(downward orientation)
Bioacoustic Microphone
Notes: Cameras in stereo allow distance and size estimates of targets

## Slide 5: Data Acquisition - ring buffer architecture
Oldest data
Data Streams
20 sec buffer
Save data 10 s before to 10 s after trigger event to permanent file.
Problem: Optics alone generate 20 TB Data/day
Solution: Event based trigger of data recording
Newest data
Event Detector
Presence
  Real time image processing
Collision
  Accelerometers
  Contact Microphones
Acoustic detectors
Notes: Camera data stream enter
circular buffer,
user defined, for example 20 sec
Watching the data stream: event detection systems – critical potential even for low resolution IR
Event detected
Records another 10 sec, from oldest to newest
Really good success with this and would recommend the data structure.

## Slide 6
North American Wind Research and Training Center
Tucumcari, NM
National Wind Technology Center
Golden, CO
1.5 MW GE
600 kW CART 3
Experimental Testing

## Slide 7
Field Experiments

## Slide 8
Raw data: routine shut-down
Flowers et al. 2014 METS Proc.
Contact microphone
Accelerometer

## Slide 9
Vibration Node – Impact Tests
Low impact stationary blade
Tennis ball - ~ 57 g
1 accelerometer – 3 axes

## Slide 10
GE (1.5 MW)
normal operation
Variable Background Signals: accelerometers
CART 3 (600 kW)
normal operation
CART 3 (600 kW)
idle rotation
Time (s)

## Slide 11
Impact Detection - Vibration Node
Chart: 
| Cart 3 - normal operation | GE - normal operation | Cart 3 - idle rotation
% Detected | 0.33333 | 0.52174 | 1
% of Impacts detected
72% of detected impacts observed on > 1 blade
n=6
n=4
n=23

## Slide 12
Vibration Node – Impact Tests
High impact moving blade
Tennis ball - ~ 57 g
Accelerometers & Contact Microphones – 3 blades

## Slide 13
Utah Dept. of Natural Resources
Puffin
Pelican
Shorebird
Storm-Petrel
Range of Bird and Bat Sizes - Offshore
Albatross
Hoary Bat
10 g …….………..800 g………………. 6,000 g
© John Avise
Western Gull

## Slide 14
Optical Node - Impact Tests
IR camera
FLIR A655sc
640 X 480
10-12 fps
Visual Camera
Allied Vision, Manta 201‐C
1624 X 1234
6 fps
Ball fired from air cannon on ground

## Slide 15
Optical Node - IR Image Analysis

## Slide 16
Optical Node –
Target Resolution
Marbled Murrelet
Length: ~24 cm
(For a 640 X 480 IR camera)
15º FOV lens
45º FOV lens

## Slide 17
Optical Node – Camera Positioning

## Slide 18
Bioacoustics Node
Silver-haired bat
Firing and impact of a tennis ball on a stationary blade

## Slide 19
Bioacoustics Node
Cart 3 Normal Operation
microphone INSIDE nacelle with impact
Accelerometer
Impact acoustic signal masked

## Slide 20
Bioacoustics Node
Cart 3 Idle Operation
microphone OUTSIDE nacelle with impact
Accelerometer
Impact acoustic signal detected!

## Slide 21
Vibration Node:
Impaction detection dependent on background signals and impact kinetics
Optical Node:
Target identification will depend on frame rate and pixel resolution, ideal placement may be on blades
Bioacoustic Node:
Valuable for impact and environmental assessment (e.g., rain, lightning, etc.), in addition to species identification
Summary
*Design & Initial Tests Very Promising*

## Slide 22
Incorporate newer, smaller, low power sensors.
Continue developing operational software and automated event detection.
Extended deployment on commercial scale, grid connected, onshore turbine.
Work with manufacturers to build sensors into turbine design.
Future Directions

## Slide 23
Integrated sensor array capabilities thus far show promise and will be instrumental during:
Site assessments for proposed facilities
Conducting impact assessments of established wind facilities
Assessing efficacy of operational mitigation or deterrent technologies.
Operational monitoring of turbine
Conclusions

## Slide 24
Funding:
US Department of Energy
Oregon State University
University of Washington
Collaborators and Advisors:
• Mesalands Community College
• H.T. Harvey & Associates
• ABR, Inc. Environmental Research &
Services
• Floating Power, Inc.
• Principal Power, Inc.
• CCAP – Coastal Energy Project
• NREL, National Wind Technology Center
• Bat Conservation International
Acknowledgements

## Slide 25: The Optical Node
Visual
Infrared
1G Ethernet switch
Visual
Infrared
Power distribution
On turbine pan and tilt mount
Travel profile

## Slide 26: System specifications
Thermal Infrared
Model
Resolution
Visual
FLIR A615sc
1 Gbit Ethernet
Lens FOV
Interface
Trigger
Frame rate
Manta G-210
12 fps
1 Gbit Ethernet
Hardware
Cost
Bandwidth
~ $ 20 k
~ 1 Gbps
15° x 12°
640 x 480
50 fps
0.25 Gbps
Software
1624 x 1234
~ $ 3 k
Software Infrastructure: Labview
52° x 45°
Notes: Coming back to the question of effectiveness, I’d like to now describe the system we used.
Model:
Ifrared Camera
380 meters away from turbine – discuss application later
Unfortunately, FLIR only subject to software trigger
IF we wan to answer the question of whether the added value of stereo IR worth that additional cost?

## Slide 27
Optical Node - Impact Tests
IR camera
FLIR A655sc
640 X 480
10-12 fps
Visual Camera
Allied Vision, Manta 201‐C
1624 X 1234
6 fps
Ball thrown from nacelle

## Slide 28
Signal Analysis
Break-down multi-frequency signal and detect single events (non-frequency domain)
Continuous wavelet transform (CWT) brakes signal into wavelets
  Construct a time-frequency representation of a signal for time and frequency localization
Real-valued wavelet
Flowers et al. 2014 METS Proc.