## Slide 1: Flare Reduction Technique for Near-Surface Airfoil Boundary Layer Measurements with Laser Diagnostics
Dongyun Shin
Daniel R. Cadel
K. Todd Lowe

## Slide 2: About project
GE Power & Water
Near-wall measurement can lead to more accurate models and design tools for new blade design
http://www.gereports.com/
http://www.windpowermonthly.com/
Boundary layer measurement is difficult but it is valuable
Minimum drag
Higher efficiency
Better performance

## Slide 3: Outline
External Illumination background
Literature review
Surface treatment development
Transparent laminate model
PIV results
Summary
Future task

## Slide 4: External Illumination background
Objective : To minimize the laser flare from the surface
Laser Flare
Light scattered/reflected off the solid surface of the airfoil saturates corresponding pixels on the camera sensor, as well as surrounding pixels in the boundary layer
Methods
scatter
absorption
transmission
Specular reflection
Fluorescent coating
Transparent airfoil
Absorb incident light
Transmit incident light

## Slide 5: Literature review

## Slide 6: Absorption: Fluorescent Paint
Silicone
Flat White paint + Rh6G + Al2O3+ ethanol
Flat Black paint + clear paint (x1)
Clear paint + Rh6G + ethanol (6 coat)
Mirror finish
Aeroglaze z306
Transparent Black paint + Rh6G + ethanol + clear paint
1
2
6
5
4
3
9
8
7
13
12
11
10
14
16
15
19
18
17
20

## Slide 7: Light intensity results
Note that the dark offset is 100 counts

## Slide 8: Stability Wind Tunnel Configuration (SWT)
Tested in SWT with Doppler Global Velocimetry
Fluorescent paint mixed and airbrushed onto metal laminate immediately prior to test run
Reynolds number
  1.5M
  2M
  3M
Laser power : 6 W
Exposure time : 2 s
AoA : -15 deg
DU96 airfoil model
Cam 1
Cam 2
Cam 3

## Slide 9: Measurement in SWT (Doppler Global Velocimetry)
Laser
Iodine cell
Data acquisition
Computer
Frequency to Intensity
532nm filter
532nm
532nm
Raw image
Treated surface
(For DGV measurement)
camera
570nm

## Slide 10: Assessments
Lab development
Untreated region
Treated region
Laser
Paint
Stability Wind Tunnel measurements
Flare appeared several millimeters above surface.
Indicated need for
grazing view angles
Cam1
Cam3
Aluminum plate

## Slide 11: Transmission: Transparent laminate
3D printed airfoil segment, transparent plastic material (Acura 60)
DU 96 airfoil model with transparent segment
Test in Open Jet Wind Tunnel has been done before SWT test

## Slide 12: Final Design
Application of the Rh6G-based fluorescent paint to the trailing edge of the transparent laminate using a standard airbrush. Paint was applied in situ
Camera calibration procedure using a LaVision type 31 dual-plane calibration plate.
Open Jet Wind Tunnel (blower type)
- 0.7m x 0.7m exit area
- Powered by 30hp BC-SW Size 365 Twin City centrifugal fan
- Maximum fan speed of 1180 RPM – flow exits the 5.5:1 contraction at 30m/s

## Slide 13: Particle Image Velocimetry (PIV)
http://www.lavision.de/en/techniques/piv.php
- Acquires consecutive images of the flow
- Spatially cross-correlation to determine pixel shift of particles
- Output velocity field with vectors

## Slide 14: PIV experiment set up
14
camera
airfoil
U∞
Laser pulse
C-Clamps
Cylindrical lens
Mirror
Transparent segment
90 degrees of angle between the camera lens and the plane of the airfoil surface
Grazing angle
The Photron SA-4 Fastcam is located at a grazing angle directly above the trailing edge of the airfoil
90°
camera
Airfoil surface
z
y
x
x
z
Laser

## Slide 15: Data processing
5000 images were acquired at a rate of 5 kHz.
Sequential planar PIV processing was performed using a multi-pass interrogation window of 32x32 pixels (first pass) and 24x24 pixels (second pass).
AoA | Re | PIV Type | Laser Current | Laminate | Surface Treatment
0° | 887,000 | Sequential | 39 A | Aluminum | None
0° | 887,000 | Sequential | 39 A | Aluminum | Rh6G paint
0° | 887,000 | Sequential | 39 A | Transparent | None
0° | 887,000 | Sequential | 39 A | Transparent | Rh6G paint
The test matrix of airfoil material and surface treatment combinations

## Slide 16: Raw images
Untreated metal laminate
Treated metal laminate
Untreated transparent laminate
Treated transparent laminate

## Slide 17: Raw Image Intensity Profiles
4096 counts for saturation
Rh6G treated transparent laminate provides the best near-wall measurement
12-bit sensor of the Photron camera
Treated transparent laminate

## Slide 18: PIV results
Untreated metal laminate
Treated metal laminate
White regions  no valid data
Cross correlation algorithm
  Validate a zero velocity when interferences exist
  Low flow velocity near the surface
Masking out the flared pixels

## Slide 19: Velocity contour
Masking-out applied
- Only 500 images were used for processing at 5kHz.
- Burning was observed as the paint heated up. Flare expanded over time.
Treated transparent laminate
Treated metal laminate

## Slide 20: Summary
Key lessons from development
Rhodamine 6G paint mixture provides best fluorescence performance
Grazing angle configuration should always be used when feasible
Masking step during processing removes bias errors from flare
For perfect grazing angles:
    Treated Transparent > Untreated Transparent > Treated Metal > Untreated Metal
For realistic camera angles (not perfect grazing angles):
    Treated Transparent > Treated Metal > Untreated Transparent > Untreated Metal
Treated Metal
Treated transparent
Grazing angle view
Airfoil TE
Future Task
Scale-up to Stability Wind Tunnel
Need to measure the surface roughness of the paint

## Slide 21: Question ?

## Slide 22: Supplemental Slides

## Slide 23: Lab experiment set up
Pco.egde
Painted surface
Nd:YVO4 laser
Black board

## Slide 24: Model Surface Options
Optimal performance with transparent laminate and fluorescent treatment
With metal laminate and fluorescent treatment, still significant benefit
  Measurements within ~3mm of the surface
Untreated metal
Treated metal
Treated transparent

## Slide 25: Burning issue
Possible solution : High temperature paint
Treated transparent TE
Images of the paint burning

## Slide 26: Absorption: Fluorescent Paint
1
2
6
5
4
3
9
8
7
13
12
11
10
14
16
15
19
18
17
20
A
B
Flat White paint + Rh6G + Al2O3
A  Without Ethanol
B With Ethanol
Rh6G is dissolved completely with ethanol
Silicone
Black Electric Tape
Flat White paint + Rh6G + Al2O3+ ethanol
Flat Black paint + Rh6G + Al2O3 +ethanol
Clear paint + Rh6G + Al2O3+ ethanol
Flat Black paint + clear paint (x1)
Flat Black paint + Rh6G + ethanol + clear paint (x1)
Clear paint + Rh6G + ethanol (x6)
Clear paint + Rh6G + ethanol (x4) + Black vinyl
Flat Black paint + Rh6G + ethanol (x6)
Flat Black paint + Rh6G + ethanol + clear paint (x2)
Flat Black paint + Rh6G + ethanol (x6) + clear paint (x2)
Clear paint + Rh6G + ethanol (x4) + Mirror finish
Mirror finish
Transparent Black paint + Rh6G + ethanol
Clear paint + Rh6G (x2) + ethanol
Aeroglaze z306
Transparent Black paint + Rh6G + ethanol + clear paint
Transparent Black paint + Rh6G (x2) + ethanol + clear paint
Aeroglaze + Rh6G + ethanol

## Slide 27: Light intensity results
Note that the dark offset is 100 counts

## Slide 28: Treated transparent laminate
Masking applied
No Masking applied

## Slide 29: Boundary layer profiles

## Slide 30: Boundary layer profiles

## Slide 31: Literature review (camera angle)

## Slide 32: Laser model
DM30-527-DH