## Slide 1: Understanding Model Uncertainty—An Application of Uncertainty Quantification to Wind Energy
Larry Berg1, Ben Yang1,2, Yun Qian1, Po-Lun Ma1, Sonia Wharton3, Vera Bulaevskaya3, Huiping Yan1, and Will Shaw1
1Pacific Norwest National Laboratory
2School of Atmospheric Sciences, Nanjing University
3Lawerence Livermore National Laboratory

## Slide 2: Motivation
US Department of Energy (DOE) is planning a second Wind Forecast Improvement Project (WFIP2)
Focused on improving simulations of wind and power in areas of complex terrain via improvements in model physics
A wide range of measurements are possible
  What are the key parameters within the surface and boundary-layer parameterizations?
Use Uncertainty Quantification (UQ) to identify important parameters
  Effort focused on what is going on “under the hood”, not combinations of different physics packages
Notes: MYNN=Mellor-Yamada-Nakanishi-Niino

## Slide 3: What is Uncertainty Quantification?
Parameterizations in atmospheric models include a large number of assumed parameters
  How sensitive are our results to these values or their functional form?
  Example from MYNN PBL scheme (for calculation of momentum flux)
Systematic approach to determine the model sensitivity to a wide number of parameters
  A smarter way than varying one parameter at a time
Length Scale
TKE
Stability Function

## Slide 4: UQ Methodology
Selected MYNN PBL scheme (e.g. Nakanishi and Niino 2009) and Revised YSU Surface Layer (Jiménez et al. 2012) scheme
  Widely used in research applications and by industry scientists
  Identified 26 parameters
Defined range of values
  Based on literature or scientific intuition
  Checks to make sure ranges stay realistic—some parameters depend on others in complicated ways
Run simulations using a wide range of values
  Select values in a smart way (via quasi-Monte Carlo sampling) to explore parameter space and limit the number of simulations required
  Simulations completed for a single month (May)
Construct Generalized Linear Model (GLM) based on full simulations for statistical analysis

## Slide 5: Experimental design
Revised YSU SFC scheme 14 parameters: zo, K, Monin-Obukhov stability functions
MYNN PBL scheme 12 parameters: TKE dissipation rate, TKE diffusion, Pr number, closure constants, length scales
Quasi-Monte Carlo (QMC)—Determine parameter values to use in WRF simulations
256 sets of simulations: WRF @ 3.3 km resolution
WRF parent simulations at 10-km resolution (with nudging)
Generalized linear model (GLM) analyses
Derive a subset of the most important parameters

## Slide 6: Study Area and Terrain Height
Inner domain
Stateline Wind Energy Center:
454 660-KW Vestas V-47 Turbines
300-MW installed capacity
Focused on the site of the Columbia Basin Wind Energy Study (CBWES)
  Conducted in an operating wind farm in north-central Oregon.

## Slide 7: Impact on Wind Power
Wind speed and wind power predictions are highly sensitive to the values of PBL Parameters

## Slide 8: Impact on Wind Power
Wind speed and wind power predictions are highly sensitive to the values of PBL Parameters
Spread in wind speed
Spread in power

## Slide 9: Sensitivity of 80-m Winds to Boundary-Layer Parameters: Relative Contribution (Daytime)
TKE dissipation rate
TKE Diffusion
Closure Constants
Length Scales
Pr Number

## Slide 10: Sensitivity of 80-m Winds to Boundary-Layer Parameters: Relative Contribution (Nighttime)
June 11, 2015
10
TKE dissipation rate
TKE Diffusion
Closure Constants
Length Scales
Pr Number

## Slide 11: Sensitivity of 80-m Winds to Boundary-Layer Parameters to Terrain Slope
Daytime
Nighttime
TKE dissipation rate
TKE Diffusion
Pr Number
Closure Constants
Length Scales
Length Scale Exponent
Length Scale Factor

## Slide 12: Response of 80-m wind to PBL parameters at CBWES
Daytime
Nighttime
Anomaly wind speed: Difference from average over the study period
TKE Dissipation Rate
Length Scale Factor
Pr Number
Length Scale Exponent
Variability associated with other parameters
Variability associated with parameter

## Slide 13: Response of 80-m wind to PBL parameters at all sites
Daytime
Nighttime
TKE Dissipation Rate
Length Scale
Factor
Pr Number
Length Scale
Exponent
Hanford
CBWES
Big Horn
Pebble
Springs
Consistent Results for All Locations

## Slide 14: Sensitivity of 80-m Winds to Surface Parameters: Relative Contribution
Main factors: z0 and k
z0
z0
k
k
Elevation

## Slide 15: Summary and Conclusions
A UQ study has been completed to investigate the sensitivity of WRF simulations to a number of parameters used in the surface and PBL schemes
  Range in wind speed yields large variability in wind power
Largest sensitivities were found for z0, TKE dissipation rate, TKE length scales, and Pr number
  Sensitivity to TKE dissipation rate and TKE length scales also function of terrain slope
New field studies should be designed to constrain these values, including measurements of:
  z0: accurate wind speed profiles and/or drag plates
  TKE throughout the PBL depth
  Parameters used in the M-O stability functions for stable conditions
Next steps: expand analysis to use additional time periods and PBL and/or surface schemes
POC: larry.berg@pnnl.gov

## Slide 16: Conclusion
Notes: Add something about spatial distribution.
What about land surface models? We could also vary

## Slide 17: Sensitivity of 80-m Winds to Surface Parameters: Relative Contribution
Main factors: z0 and k
Daytime (6-18 LST)

## Slide 18: Sensitivity of 80-m Winds to Surface Parameters: Relative Contribution
Main factors: z0 and k
Daytime (6-18 LST)
Relative Contribution: z0
Relative Contribution: Von Karman

## Slide 19: Sensitivity of 80-m Winds to Surface Parameters: Relative Contribution
Main factors: z0 and k, increased dependence on M-O functions
Nighttime (18-6 LST)

## Slide 20: Identification of Surface Parameters
Parameter name | description | default value | estimated range
x1 | X=(1.-16.*zolf)**(1/4) Used for the calculation of psim_unstable | 16 | (14, 18)
x2 | X=(1.-16.*zolf)**(1/4) | 4 | (3.5, 4.5)
y1 | Y=(1.-16.*zolf)**(1/2) Used for the calculation of psih_unstable | 16 | (14, 18)
y2 | Y=(1.-16.*zolf)**(1/2) | 2 | (1.5, 2.5)
ym1 | YM=(1.-10.*zolf)**(1/3) Used for the calculation of psim_unstable | 10 | (9.7, 11.6)
ym2 | YM=(1.-10.*zolf)**(1/3) | 3 | (2.5, 3.5)
yh1 | YH=(1.-34.*zolf)**(1/3) Used for the calculation of psih_unstable | 34 | (26, 42)
yh2 | YH=(1.-34.*zolf)**(1/3) | 3 | (3.0, 3.5)
ms1 | psim_stable=-6.1*log(zolf+(1+zolf**2.5)**(1./2.5)) | 6.1 | (4.8, 9.4)
ms2 | psim_stable=-6.1*log(zolf+(1+zolf**2.5)**(1./2.5)) | 2.5 | (1.1, 2.5)
hs1 | psih_stable=-5.3*log(zolf+(1+zolf**1.1)**(1./1.1)) | 5.3 | (4.5, 9)
hs2 | psih_stable=-5.3*log(zolf+(1+zolf**1.1)**(1./1.1)) | 1.1 | (1.1, 2.5)
znt_factor | znt_new=znt*znt_factor | 1 | (1.0, 2.0)
karman | Von Karman constant | 0.4 | (0.35, 0.4)

## Slide 21: Identification of Boundary-Layer Parameters
Parameter name | description | default value | estimated range
b1 | used in definition of the dissipation rates | 24 | (12,36)
sqfac | TKE Diffusion factor | 2 | (1.5, 4.5)
pr | turbulent Prandtl number | 0.74 | (0.5, 2)
c3 | closure constant | 0.34 | (0.33, 0.5)
c5 | closure constant | 0.2 | (0.1, 0.3)
g1 | closure constant | 0.229 | (0.1768, 0.2395)
alp1 | Used in calculation of the turbulence length scale (LT) | 0.23 | (0.115, 0.345)
alp2 | Used in calculation of the turbulence length scale (LB) | 0.65 | (0.5, 1.0)
alp3 | Used in calculation of the turbulence length scale (LB) | 3 | (2.5, 7.5)
alp4 | Used in calculation of the turbulence length scale (LS) | 20 | (20, 100)
cns | Used in calculation of the turbulence length scale (LS) | 2.1 | (1.35, 4.05)
ls_exp | Exponent on equation to determine LS that is based on results from LES | 0.2 | (0.1, 0.3)
Closure
Constants
Length Scales
TKE dissipation rate
TKE Diffusion
Pr Number