## Slide 1
Low Level Jet properties
from lidar measurements
in the Gulf of Maine
Yelena Pichugina1, 2, Robert Banta2 , Alan Brewer2, Aditya Choukulkar1, 2, Melinda Marquis2, Mike Hardesty1, 2,
Ann Weickmann1, 2, and Scott Sandberg2
1Cooperative Institute for Research in Environmental Sciences, Boulder, CO
2National Oceanic and Atmospheric Administration, Boulder, CO
NAWEA June 11, 2015

## Slide 2
LLJ features from lidar measurements
LLJ
sunset
midnight
1:00
2:00
3:00
4:00
5:00
6:00
7:00
8:00
9:00
σ2 (m 2 s-2)
U (m s-1)
U (m s-1)
σ2 (m 2 s-2)
Notes:     Low Level Jets (LLJs) are well known phenomena in the Great Plains
  Frequently occurred within the rotor layer
  Winds at higher height separate from the lower layer near the surface and accelerate creating the LLJ
  Strong wind shear trough the layer of the turbine blades span
  The strong shear below jet maxima produces larger values of turbulence
  LLJ importance for Wind Energy operations
A major source of wind power and shear-generated turbulence
Damaging impact on wind turbines through increased loads and fatigue

## Slide 3
    Motivation
    Could LLJs be observed offshore?
    frequency, strength, height
    Magnitude of shear within rotor layer?
    How accurate are hub-height winds calculated from surface measurements?
    Power estimates based on hub-height wind speed vs rotor equivalent wind speed

## Slide 4
NOAA Research Vessel
Lidar measurements from the
New England Air Quality Study (NEAQS)
July 09-August 12, 2004
Pointing angle error
< 0.5º - normal sea
< 1º - rough sea
Notes: The experiment was designed to track urban pollution plumes

## Slide 5
Lidar dataset:
15-min averaged profiles of wind speed and direction
Profiles of wind speed and direction
About 2000 profiles of wind speed were analyzed to indicate LLJ properties (frequency, strength, height of jet maxima), and
wind shear through the layer of 50-150 m
Notes: Google map image of ship tracks during the NEAQS-04 experiments. Each yellow dot represents individual location of lidar measurements at a given time. A better resolution map, inserted on the bottom right corner, illustrates data points in the dense-measurement areas.

## Slide 6
LLJs along ship tracks
August 11

## Slide 7
mean=9.4 m s-1
median=8.7 m s-1
LLJ speed
LLJ height
mean=156.6 m
median=124.7 m
72% of 15-min wind speed profiles show LLJs

## Slide 8
50 m
100 m
150 m
100 -150 m
50 -150 m
50 -100 m
Wind speed shear
Wind speed
Wind directional shear
Wind direction
Mean shear through the rotor layer
(July 9 - August 12)
Wind shear stronger:
- at night hours
- below hub-height
Wind directional shear is not significant

## Slide 9
U=UREF(Z/ZREF)α
Surface and hub-height winds
10 m
100 m
10 m 100 m

## Slide 10
Measured and computed winds at 100 m
Experiment- mean power bias:
0.23 MW (α =0.10)
0.42 MW (α =0.07
∆ws (m s-1)
∆P (MW)
P=1/2 ρ AU3CP
ρ =1.23 kg/m air density
CP = 0.4 (power coefficient)
A= 7850 m2 (circle area, π R2)
Notes: The experiment-mean biases of 0.23 and 0.43 MW indicate losses in the power prediction for this period by using power-law relations with shear exponent (α) of 0.1 or 0.07, respectively. For sample period of August 11 (Fig.3.1) the bias in the power production were 1.6 and 2.2 MV, respectively.

## Slide 11
Can a value of the shear exponent (α) be found from measurements?
mean: 0.16
median: 0.15
count: 1624
0.07
0.16
0.19
0.12
0.1

## Slide 12
NOAA models used in the study
Rapid Refresh RAP 13 km
High Resolution Rapid Refresh HRRR 3 km
North American Mesoscale RR NAMRR 12 km
NAMRR Contiguous United States NAMRR Conus 4 km
Prediction of Offshore
Wind Energy Resources (POWER)

## Slide 13
Greater discrepancies - for LLJ-like profiles
02:00
03:00
04:00
05:00
02:00
03:00
04:00
05:00
Lidar
RAP, HRRR
NAM P, NAM C
July 16
August 9
Examples of lidar-measured and modeled wind profiles

## Slide 14
Shear through the rotor layer
In all cases power estimates using hub-height winds can produce significant errors

## Slide 15
Techniques to compute the rotor equivalent wind speed
(1)
(2)
Wagner et al., 2009
Choukulkar et al., 2015
Notes: It was shown (Wagner 2009) for winds over flat terrain, that the correlation between the electrical power and the wind speed
improved as the electrical power was plotted as a function of a weighted wind speed measured at more points
on the vertical over the turbine swept rotor area. But their work did not include the inﬂuence of parameters like wind direction and
turbulence variations.

## Slide 16
mean:
1.04%
1.49%
mean:
51.kWT
52 kWT
Normalized bias of wind power computed by the hub-height and the rotor equivalent wind speed

## Slide 17
Conclusions
Wind profiles obtained from ship-borne Doppler lidar measurements often show LLJs within turbine rotor heights
- more frequently during nighttime hours
The maximum of jet speed varies from 5 to 20 ms-1, with the mean value of 9.4 ms-1
Jet heights are spread up to 600 m, with the mean value of 156.6 m
LLJs can significantly modify wind profiles producing vertical wind-shear of 0.03 s-1 or more across the rotor layer of 50-150 m
Extrapolation of near-surface winds to hub height power-law relation show biases of 0.25 s-1
The shear exponent (α), found from lidar data, show diurnal variations from 0.1 to 0. 25, with the mean value of 0.16 for the entire experiment
A two techniques for calculating rotor layer equivalent wind were tested and show 1-1.5% less power compare to the power estimated by hub-height wind.

## Slide 18
Thank you!
Questions?
Yelena.Pichugina@noaa.gov

## Slide 19
(PW – PT)/PH
mean: 3.52 kWT
mean: 0.45%
Normalized bias of the power based on the rotor equivalent wind computed by using 2 techniques

## Slide 20
The summer period during the experiment was characterized by the low winds and the wave height averaged over 10 years
Data from the Lighted Buoy BF NOAA 44013, located 16 n miles east of Boston
(www.ndbc.noaa.gov)
The NCBD buoy’s data
Buoy-based sonic anemometer measurements are not representative of the higher elevation winds due to the unknown shear/stability profiles [Sienkiewicz, 2014]

## Slide 21
ZREF=10m
α=0.16
α=0.07
α=0.10
α=0.14
α=0.20
α=0.25
ZREF=25m
ZREF=15m
ZREF=35m
Time series of the bias between measured hub-height wind and computed by the power-law by using six different values of shear exponent (α) as indicated by the color bar at the top of the figure. The referenced wind used in the computations are also lidar measured wind at the referenced height (ZREF) as indicated on the each panel. Black lines and black diamond symbols in each panel show difference between winds measured at hub-height and referenced height.
ZREF=55m
ZREF=45m
The bias between measured hub-height wind and computed by the power-law by using different values of shear exponent and referenced heights