## Slide 1: Modeling the variability of renewable generation and electrical demand in RTOs and cities using reanalyzed winds, insolation and temperature
Photo by Bob Henson (UCAR)
Daniel Kirk-Davidoff1,2,
Stephen Jascourt1,
Chris Cassidy1 1MDA Information Systems LLC 2AOSC, University of Maryland

## Slide 2: US and Canadian RTO/ISO regions
BPA

## Slide 3: Wind Farms in the US
Image courtesy of AWEA

## Slide 4
National Scale Wind Generation in near-real time

## Slide 5
Generating an historical renewable generation index
The need: Energy traders and other electrical market participants need a consistent measure of wind generation in real electrical markets that represents the variability in electrical generation associated with weather fluctuations, and not changes in wind generation infrastructure. Such an index allows accurate assessment of the probability distribution of generation over the coming year, month, or week.
The solution: a procedure to generate a virtual history of wind generation for each electrical interconnection for past 30 years using an up-to-date, frozen wind generation infrastructure.
Each year, we can regenerate the 35+ year climatology of wind generation that would have resulted from the real wind variations over that period acting on the wind generation infrastructure of the present day.

## Slide 6
Schematic of Wind Index Production
Wind Farm Locations and Properties
Reanalyzed Wind Speeds (1979-2011)
Observed Wind Generation Data (2011)
Simulated Wind Generation History
Tuned Model
Wind Turbine Power Curves
Climate Indices
(ENSO, NAO, MJO)
Dynamical Wind Generation Prediction
Coupled climate prediction model
Statistical Wind Generation Prediction
Generating an historical renewable generation index

## Slide 7
Wind Farm Locations & Properties
In this study, we will generate simulated historical wind and solar power generation for the AESO and IESO ISOs in Canada, and for the BPA, CAISO, ERCOT, MISO, PJM and SPP transmission organizations in the US.
We use a parametric power curve that allows for arbitrary values of the cut-in, rated and cut-out wind speeds.
Farm locations and generation capacity are indicated by dots, scaled by size (largest is 444 MW). Total capacities are 13 GW in ERCOT, 15 GW in MISO

## Slide 8
Solar Generation
Notes: Because solar generation is still relatively small in the US, we use a simpler approach here to simulate its variability. We interpolate CFSR surface insolation values to the six largest population centers in each RTO, and then scale the total generation (weighted by population) so that the maximum power generated is equal to the maximum wind generation in each RTO. We’ve looked at the ability of the CFSR to reproduce variability at the Surfrad sites, and it’s adequate, as shown in the figure below.

## Slide 9
Simulated Wind Generation History
These plots show hourly wind generation for the ERCOT and MISO interconnections. Blue shows the simulated wind generation, green shows the actual generation. The agreement is quite good: correlation coeffcients are 0.91 and 0.94 for ERCOT and MISO respectively.

## Slide 10
Simulated Wind Generation History
These plots show hourly wind generation for the ERCOT and MISO interconnections. Blue shows the simulated wind generation, green shows the actual generation. The agreement is quite good: correlation coefficients are 0.91 and 0.94 for ERCOT and MISO respectively.

## Slide 11
Simulated Wind Generation History
Here are the full 30 year histories, smoothed to monthly means for clarity.

## Slide 12
Simulated Wind Generation History
In these plots the annual cycle has been removed, to show the anomalous monthly mean generation in each interconnection.
A small, but significant trend of 85 MW/decade is evident in the ERCOT history, while the MISO history shows no significant trend.
Notes: Climate model simulations of wind under anthropogenic climate change show some trend towards increasing wind power in central United States, due to an increase in storminess (rather than to any increase in the mean westerly flow).

## Slide 13
Reanalyzed Demand
We can also simulate the weather-dependent part of electrical demand using reanalysis temperature data (weighted by population) and actual demand data. Of course we could just use actual demand data as well, but we want to isolate the contribution of weather variability here.
Electrical Demand Simulation

## Slide 14
Reanalyzed Demand
We can also simulate the weather-dependent part of electrical demand using reanalysis temperature data (weighted by population) and actual demand data. Of course we could just use actual demand data as well, but we want to isolate the contribution of weather variability here.
Electrical Demand Simulation

## Slide 15
Climatology of Historical Wind Generation
Here we show the average of 32 years of simulated wind generation history, by hour of year.
This shows well the change in the amplitude of the diurnal cycle, as well as the change in daily mean generation through the seasonal cycle.
Simulated Wind Generation History

## Slide 16
Climatology of Historical Wind Generation
Here we show the average of 32 years of simulated solar generation history, by hour of year.
Simulated Solar Generation History

## Slide 17
Climatology of Historical Wind Generation
Here we show the average of 32 years of simulated total renewable (solar + wind) generation history, by hour of year.
Simulated Renewable Generation History

## Slide 18
Climatology of Historical Electrical Demand
Here we show the average of 32 years of simulated temperature-dependent electrical demand, by hour of year.
This shows well the change in the amplitude of the diurnal cycle, as well as the change in daily mean generation through the seasonal cycle.
Simulated Electrical Demand History

## Slide 19
Climatology of Historical Electrical Demand
These figures show demand with renewable generation subtracted.
Simulated Electrical Demand History

## Slide 20
Climatology of Historical Electrical Demand
These show demand minus renewable generation for 35% renewable penetration in each RTO/ISO.
Simulated Electrical Demand History

## Slide 21
Here we show two-dimensional histograms of wind generation (horizontal axis) and temperature-dependent electrical demand (vertical axis). For reference, the same map for two log-normally distributed random variables is shown below. Some of the relationships (MISO) are “worse” than random, in the sense of preferentially low generation during times of high demand and vice versa, while others are “better” (AESO, PJM).
Correlation of Wind and Demand

## Slide 22
Here we show two-dimensional histograms of solar generation (horizontal axis) and electrical demand (vertical axis). Correlations range from 0.03 in BPA to 0.72 in ERCOT.
Correlation of Solar and Demand

## Slide 23
Here we show two-dimensional histograms of total renewable generation (wind + solar, horizontal axis) and electrical demand (vertical axis). Correlations range from 0.00 in BPA to 0.48 in ERCOT.
Correlation of Renewables and Demand

## Slide 24
Generation Droughts

## Slide 25
Generation Droughts

## Slide 26
Generation Droughts

## Slide 27
Generation Droughts

## Slide 28
Over-all variance for present wind, scaled solar

## Slide 29
Over-all variance for 25% renewable generation

## Slide 30
Over-all variance for 35% renewable generation

## Slide 31
Conclusions
Renewable generation (solar, wind and combined) variability has very different characteristics in different regions.
Reanalysis does a good job reproducing wind generation and demand variability. High resolution is probably not necessary, given our ample observed generation record.
Determination of reanalysis’s ability to reproduce subtler aspects of solar variability will have to wait for more installed capacity for validation.
A thirty year record of simulated generation allows improved estimates of rare events vis-à-vis a shorter record, but the advantage isn’t overwhelming